## Slide 1
NVMe over MPTCP
Multi-Fold Acceleration for NVMe over TCP
in Multi-NIC Environments
Geliang Tang - MPTCP Community
Kylin Software
LSF/MM/BPF 2026
Zagreb, May 2026
1/15
Notes: Hello everyone. I'm Geliang from the MPTCP community. I'm one of the
core upstream developers of MPTCP since 2020. I live in Beijing, China
and work at a Chinese Linux distribution company, called Kylin Software.
Here I bring a proposal to add MPTCP support for NVMe. This approach
achieves a multi-fold /ˈmʌl.tɪ.fəʊld/ performance improvement over using NVMe TCP in
multiple /ˈmʌl.tɪ.pl/ network devices environments.

## Slide 2
Thanks to Hannes Reinecke, Matthieu Baerts, Mat Martineau, Paolo Abeni, Coly Li, Barry Song, Ming Lei, Zhenwei Pi, Jason Xing, Hui Zhu, Gang Yan, and others for their help during the development of NVMe over MPTCP.
2/15
Notes: First of all, I want to say thanks to everyone who helped me during the
development of this feature.

## Slide 3
Introduction to MPTCP
Agenda
Motivation
Current Status
Performance Evaluation
Implementation
Discussion
3/15
Notes: And here is the agenda /əˈdʒen.də/. First, I'll give a very brief introduction to MPTCP.
Then the motivations of NVMe MPTCP. Next, I'll show the patch list of all
the changes. Then I'll show a demo /ˈde.məʊ/ of how to use NVMe MPTCP, and
what the benefit is. Next, how NVMe MPTCP is implemented. And the last is the
discussion (/dɪˈskʌʃ.ən/).

## Slide 4
Introduction to MPTCP
Multipath TCP or MPTCP is an extension to the standard TCP and is described in RFC 8684.
MPTCP is implemented via TCP Options, kind number of MPTCP is 30.
It allows a device to make use of multiple interfaces at once to send and receive TCP packets over a single MPTCP connection.
MPTCP can aggregate the bandwidth of multiple interfaces or prefer the one with the lowest latency. It also allows a fail-over if one path is down, and the traffic is seamlessly reinjected on other paths.
Introduced in Linux kernel v5.6
How to use it?
  Address config: ip mptcp (manual); mptcpd daemon or NetworkManager (automatic).
  Create socket: socket(AF_INET, SOCK_STREAM, IPPROTO_MPTCP) or force with BPF.
  Use: same as TCP sockets; multiple TCP subflows are created in kernel space to send and receive data.
For more details, please visit the project website: https://www.mptcp.dev
4/15
Notes: Here I will give a very brief introduction to MPTCP.
MPTCP, or Multipath TCP, is an extension to the standard TCP and is
defined in RFC 8684. MPTCP is implemented via TCP options. A dedicated
TCP option is defined for MPTCP, and its kind number is 30. It allows a
device to use multiple network interfaces at the same time to send and
receive TCP packets /ˈpæk.ɪt/ over a single connection.
MPTCP can be used for combining the bandwidth of multiple interfaces or
choosing the best path with the lowest latency. It also supports
fail-over /ˈfeɪl/: if one path goes down, traffic is smoothly switched to another
path without interruption.
It was introduced in Linux kernel 5.6. After more than six years of
development, it has become mature /məˈtʃʊə/ and stable, and more and more
network applications already support MPTCP.
How to use it?
First, we need to do address /əˈdres/ configuration, which is handled by
the path manager. We can use 'ip mptcp' commands to do it manually,
or we can use the MPTCP daemon (ˈdiː.mən) (mptcpd) to do it automatically.
Then, we need to create MPTCP sockets both on the server side and client side.
If only one side uses MPTCP, the connection will fall back /fɔːl bæk/ to TCP.
We need to explicitly pass the protocol number IPPROTO_MPTCP (that is 262)
as the third parameter of socket() syscall to create an MPTCP socket.
Or, without changing any code, we can use the BPF tool to force a TCP
application to use MPTCP.
After the MPTCP sockets are created, we can use them just like TCP sockets,
with no difference. Inside the MPTCP protocol stack /stæk/, multiple TCP
sockets are created in kernel space to send and receive data, based on the
address configuration; we call each TCP socket a subflow.
For more details, please visit the project website: mptcp.dev

## Slide 5
Motivation
Provide a kernel-space use case for MPTCP
  -> Drives missing MPTCP features forward: .read_sock, KTLS, etc.
Achieve multi‑fold bandwidth aggregation in multi‑NIC environments
  -> Break the single-device bottleneck of NVMe TCP
Improve reliability with transparent fail-over across network paths
  -> Without adding complexity to NVMe layer
5/15
Notes: Why do we need NVMe MPTCP?
First, all current use cases for MPTCP are in userspace. NVMe TCP runs
in kernel-space. So adding MPTCP support to NVMe provides the first
kernel‑space use case for MPTCP. This helps us verify the functionality
of MPTCP from kernel space and add missing features - like read_sock
interface and TLS encryption - which were not implemented in MPTCP before.
Second, in multiple network device environments, NVMe TCP can
only use a single network device, so the bandwidth is limited by
the speed of that single device. With MPTCP, we can aggregate
the bandwidth of all available devices on both the target side and
the host side, achieving a multi‑fold performance improvement -
as we will see in the demo.
Third, MPTCP allows a fail-over. If a path fails, traffic switches
to another path without breaking the NVMe connection. So we get better
reliability without adding complexity to NVMe layer.
These are the main motivations behind this work.

## Slide 6
Current Status
The modifications in the NVMe subsystem are minimal, most of the changes are on the MPTCP side.
Here are the patchsets:
mptcp: implement .read_sock (Mainlined)
NVMe over MPTCP (Under Review)
MPTCP KTLS support (Under Review)
Enable KTLS for NVMe MPTCP (Under development)
User space changes (Under development)
Fixes for MPTCP corner cases (Under Review)
6/15
Notes: I started working on this feature about a year ago. Currently, the
implementation and testing are mostly done. Some code is upstreamed,
while most remains under review on MPTCP side, in RFC stage.
The modifications in the NVMe subsystem are minimal. Most of the code
changes are on the MPTCP side.
Here are the patchsets:
1 mptcp: implement .read_sock (/riːd/ underscore)
NVMe TCP uses read_sock interface for receiving data. However, it was
not implemented in MPTCP before /bɪˈfɔː(r)/, since all current use cases for MPTCP
are in userspace, where read_sock is not used. So my first task was to
implement this interface for MPTCP.
After several rounds of iteration, this set was merged into Linux kernel
in February this year. With this interface, we can add MPTCP support
/səˈpɔːt/ for NVMe now.
2 NVMe over MPTCP
This set adds basic MPTCP support for NVMe, but without TLS encryption /ɪnˈkrɪp.ʃən/.
It defines a new transport /ˈtræn.spɔːt/ type for MPTCP, which creates /kriˈeɪt/ MPTCP sockets
between the target (ˈtɑːɡɪt) and the host instead of TCP sockets.
This set is currently under review on MPTCP side, and today's discussion
is mainly about this set.
3 MPTCP KTLS support
MPTCP did not support TLS before. They conflict with each other to
some extent. Because both MPTCP and TLS use ULP, Upper Layer Protocol.
ULP settings, including TLS settings, are disabled in MPTCP. If you set
TLS for an MPTCP socket, you will get an error code of 'NOT SUPPORTED'.
But now NVMe needs to use TLS for encryption, it's time to enable it.
I finally found a solution to make MPTCP and TLS compatible, and
implemented MPTCP support on the TLS side and enabled TLS settings on
the MPTCP side. Need to say, only software TLS encryption is supported
for MPTCP right now; hardware TLS has not yet been developed.
This set is currently under review on MPTCP side, and I believe it will
be upstreamed this year.
4 Enable KTLS for NVMe MPTCP
Once TLS is supported /səˈpɔː.tɪd/ for MPTCP, using TLS for NVMe MPTCP becomes
straightforward /ˌstreɪtˈfɔː.wəd/. Only need to enable TLS setting in configfs
for the MPTCP transport type.
5 The next is about user space changes
User space libraries (ˈlaɪ.brər.i) and tools, including libnvme (lɪb),
nvme-cli, and ktls-utils, also need to add MPTCP support.
6 The last is fixes for MPTCP corner cases
During the development of NVMe MPTCP, some MPTCP corner‑cases were
triggered, and these bugs needed to be fixed.
That's all the patch list.

## Slide 7
Performance Evaluation (NVMe TCP)
Each network device is limited to a speed of 125 MB/s (1000 mbit/s)
# ./mptcp_nvme.sh tcp numa tls
READ: bw=112MiB/s (118MB/s), 112MiB/s-112MiB/s (118MB/s-118MB/s),
io=1123MiB (1177MB), run=10018-10018msec
WRITE: bw=112MiB/s (117MB/s), 112MiB/s-112MiB/s (117MB/s-117MB/s),
io=1118MiB (1173MB), run=10018-10018msec
7/15
This demo is the selftest script for NVMe over MPTCP
# ns1 (target) ns2 (host)
# 10.1.1.1 10.1.1.2
# 10.1.2.1 10.1.2.2
# 10.1.3.1 10.1.3.2
# 10.1.4.1 10.1.4.2
Notes: Now let's look at a demo.
This demo is the selftest script for NVMe MPTCP, it is the last patch
in the 'NVMe over MPTCP' patch set. This script takes three arguments.
The first is the transport type, which can be set to 'tcp' or 'mptcp'.
The second is the I/O policy, which can be set to 'numa',
'round-robin'(ˈrɒb.ɪn), or 'queue-depth'. The third is 'tls', which
controls whether TLS encryption is used.
This test creates two network namespaces. One is used to run the NVMe
target, that is the server side, and the other is used to run the NVMe
host, that is the client side. Each namespace has four virtual /ˈvɜː.tʃu.əl/ network
devices, and each network device is limited to a speed of 100 megabytes /ˈmeɡ.ə.baɪts/
per second.
When we run NVMe TCP in this environment, the 'fio' benchmark shows the
speed is about 100 megabytes per second, as we expected. That means
only the first network device on both sides is used for NVMe TCP
communication, and the other three network devices are unused and not
involved.
When we use NVMe MPTCP in the next slide, this is not the case at all.

## Slide 8
target:
# ip mptcp endpoint add 10.1.2.1 signal
# ip mptcp endpoint add 10.1.3.1 signal
# ip mptcp endpoint add 10.1.4.1 signal
host:
# ip mptcp endpoint add 10.1.2.2 subflow
# ip mptcp endpoint add 10.1.3.2 subflow
# ip mptcp endpoint add 10.1.4.2 subflow
Performance Evaluation (NVMe MPTCP)
# ./mptcp_nvme.sh mptcp numa tls
READ: bw=427MiB/s (448MB/s), 427MiB/s-427MiB/s (448MB/s-448MB/s),
io=4286MiB (4494MB), run=10039-10039msec
WRITE: bw=387MiB/s (406MB/s), 387MiB/s-387MiB/s (406MB/s-406MB/s),
io=3885MiB (4073MB), run=10043-10043msec
In a four-network-device environment, MPTCP achieves a four times performance improvement.
8/15
Notes: Before running NVMe MPTCP, we need to do some configuration to
tell MPTCP which IP addresses are available.
We do that with the 'ip mptcp endpoint add' commands. On both sides, we
add the IP addresses of the second, third, and fourth network devices
into the address list of MPTCP path manager. The difference is, on the
target side, we use the 'signal' flags, while on the host side, we use
the 'subflow' flags.
After this configuration, we can run NVMe MPTCP now. The 'fio' benchmark
shows the speed reached about 400 megabytes per second. That means all
four network devices on both sides are used for the NVMe MPTCP
communication. It also means that in a four-network-device environment,
NVMe MPTCP achieves a four times performance improvement.
I also did similar experiments in environments on real machines with real
network devices, and obtained the same conclusion.
How is all this achieved? Let's go to the next slide.

## Slide 9
Host Side
Target Side
ret = sock_create(port->addr.ss_family, SOCK_STREAM,
IPPROTO_TCP, &port->sock);
tcp_sock_set_nodelay(port->sock->sk); (list_add corruption)
sock_set_reuseaddr(port->sock->sk); (Address already in use)
sock_set_priority(port->sock->sk, so_priority);
sock_no_linger(sock->sk);
ip_sock_set_tos(sock->sk, inet->rcv_tos);
ret = sock_create_kern(current->nsproxy->net_ns,
ctrl->addr.ss_family, SOCK_STREAM, IPPROTO_TCP, &queue->sock);
tcp_sock_set_syncnt(queue->sock->sk, 1);
tcp_sock_set_nodelay(queue->sock->sk);
sock_no_linger(queue->sock->sk); (nvme disconnect)
sock_set_priority(queue->sock->sk, so_priority);
ip_sock_set_tos(queue->sock->sk, nctrl->opts->tos);
Implementation
TCP is currently hardcoded in a few places:
9/15
Notes: I took a very practical, engineering-style approach to implement this
feature, I first modified the socket creation code for both the target
side and host side, hardcoding the protocol number from IPPROTO_TCP to
IPPROTO_MPTCP to create MPTCP sockets by force, and then I wrote a test
script to run it, and got some failures.
The first is a crash of 'list_add corruption'. Debugging showed it
happened inside tcp_sock_set_nodelay. We cannot use the TCP version of
the set_nodelay helper on MPTCP sockets; that causes a crash. I need
to implement an MPTCP‑specific version of this helper, and use it for MPTCP sockets.
After fixing that, I continued testing. I got another error 'Address
already in use' from 'bind()' on the target side, indicating that the
reuse address (set_reuseaddr) behavior was not set correctly, so I then
implemented an MPTCP‑specific version of set_reuseaddr helper too, and used it
for MPTCP sockets.
Then on the host side the 'nvme disconnect' command sometimes failed.
That turned out to be no_linger behavior not being set correctly for
MPTCP sockets. So I implemented an MPTCP‑specific version of no_linger helper
too, and used it for MPTCP sockets.
In the end, I realized that all the helpers used to change the behavior
of NVMe sockets needed to have MPTCP‑specific versions and to be used
for MPTCP sockets. They are six helpers in total. After switching to
using all six MPTCP‑specific helpers, the tests worked well and became
stable.
Then I thought all the changes were done. I went back to think about the
code architecture.
I abstracted all the places that needed to be changed from TCP to MPTCP
into a structure, which can describe all the differences between using
TCP and MPTCP in NVMe. It includes the protocol number and the six
interfaces that change socket behavior, and then defines two different
instances of this structure for TCP and MPTCP, and then switches between
them based on the transport type.
However, there are slight differences between the interfaces on the target
side and the host side. set_reuseaddr interface is only used on the target,
while set_syncnt is only used on the host. It ended up being separated into
two structures: one for the target (nvmet_tcp_proto) and the other for the host
(nvme_tcp_proto).
Let's look at the target one first.

## Slide 10
Add a pointer to this structure in tcp_port:
Target Implementation
+static const struct nvmet_tcp_proto nvmet_mptcp_proto = {
+ .protocol = IPPROTO_MPTCP,
+ .set_reuseaddr = mptcp_sock_set_reuseaddr,
+ .set_nodelay = mptcp_sock_set_nodelay,
+ .set_priority = mptcp_sock_set_priority,
+ .no_linger = mptcp_sock_no_linger,
+ .set_tos = mptcp_sock_set_tos,
+ .ops = &nvmet_mptcp_ops,
+};
struct nvmet_tcp_port {
+ struct rcu_head rcu;
... ...
void (*data_ready)(struct sock *);
+ const struct nvmet_tcp_proto *proto;
};
+struct nvmet_tcp_proto {
+ int protocol;
+ void (*set_reuseaddr)(struct sock *sk);
+ void (*set_nodelay)(struct sock *sk);
+ void (*set_priority)(struct sock *sk, u32 priority);
+ void (*no_linger)(struct sock *sk);
+ void (*set_tos)(struct sock *sk, int val);
+ const struct nvmet_fabrics_ops *ops;
+};
if (nport->disc_addr.trtype == NVMF_TRTYPE_TCP) {
port->proto = &nvmet_tcp_proto;
} else if (nport->disc_addr.trtype == NVMF_TRTYPE_MPTCP) {
port->proto = &nvmet_mptcp_proto;
}
+static const struct nvmet_fabrics_ops nvmet_mptcp_ops = {
+ .owner = THIS_MODULE,
+ .type = NVMF_TRTYPE_MPTCP,
+ .msdbd = 1,
+ .add_port = nvmet_tcp_add_port,
... ...
+};
Define a target tcp_proto structure:
Define nvmet_tcp_proto / nvmet_mptcp_proto for TCP / MPTCP:
New transport type and fabrics ops for MPTCP:
ret = sock_create(port->addr.ss_family,
SOCK_STREAM,
+ port->proto->protocol,
&port->sock);
+ port->proto->set_reuseaddr(port->sock->sk);
+ port->proto->set_nodelay(port->sock->sk);
Initialize the pointer to a different instance based on transport type (TCP or MPTCP) in add_port callback:
Access the instance through the pointer in tcp_port, and use this instance afterwards:
10/15
Notes: On the target side, we define a NVMe target tcp_proto structure, and
put the protocol number and the five interfaces to change the behavior
of the socket into it, and define two instances of this structure for
TCP and MPTCP. Add a pointer to this structure in nvme target tcp_port.
Define a new MPTCP transport type, and a new MPTCP fabrics ops. This ops
is the same as the TCP one, only the transport type is different.
When adding a port, the add_port callback is called for both TCP and
MPTCP. In this callback, initialize the pointer in tcp_port to a
different instance based on whether the transport type is TCP or MPTCP.
Afterwards, we access the instance through the pointer in tcp_port, and
use the protocol number of this instance to create the socket and call
the corresponding interfaces of this instance to change the socket
behavior.
That is the implementation of the target side.

## Slide 11
Define a host tcp_proto structure:
Host Implementation
+static const struct nvme_tcp_proto nvme_mptcp_proto = {
+ .protocol = IPPROTO_MPTCP,
+ .set_syncnt = mptcp_sock_set_syncnt,
+ .set_nodelay = mptcp_sock_set_nodelay,
+ .no_linger = mptcp_sock_no_linger,
+ .set_priority = mptcp_sock_set_priority,
+ .set_tos = mptcp_sock_set_tos,
+ .ops = &nvme_mptcp_ctrl_ops,
+};
struct nvme_tcp_ctrl {
+ struct rcu_head rcu;
... ...
u32 io_queues[HCTX_MAX_TYPES];
+ const struct nvme_tcp_proto *proto;
};
+struct nvme_tcp_proto {
+ int protocol;
+ int (*set_syncnt)(struct sock *sk, int val);
+ void (*set_nodelay)(struct sock *sk);
+ void (*no_linger)(struct sock *sk);
+ void (*set_priority)(struct sock *sk, u32 priority);
+ void (*set_tos)(struct sock *sk, int val);
+ const struct nvme_ctrl_ops *ops;
+};
if (!strcmp(ctrl->ctrl.opts->transport, "tcp")) {
rcu_assign_pointer(ctrl->proto, &nvme_tcp_proto);
} else if (!strcmp(ctrl->ctrl.opts->transport, "mptcp")) {
rcu_assign_pointer(ctrl->proto, &nvme_mptcp_proto);
}
+static struct nvmf_transport_ops nvme_mptcp_transport = {
+ .name = "mptcp",
+ .module = THIS_MODULE,
+ ...
+ .create_ctrl = nvme_tcp_create_ctrl,
+};
Define nvme_tcp_proto / nvme_mptcp_proto for TCP / MPTCP:
Add a pointer to this structure in tcp_ctrl:
New transport ops for MPTCP:
ret = sock_create_kern(current->nsproxy->net_ns,
  ctrl->addr.ss_family, SOCK_STREAM,
+ proto->protocol, &queue->sock);
+ proto->set_syncnt(queue->sock->sk, 1);
+ proto->set_nodelay(queue->sock->sk);
Initialize the pointer to a different instance based on transport name (tcp or mptcp) in nvme_tcp_alloc_ctrl:
Access the instance through the pointer in tcp_ctrl, and use this instance afterwards:
11/15
Notes: The implementation on the host side is similar.
Define a NVMe tcp_proto structure, and put the protocol number and the five
interfaces to change the behavior of the socket into it, and define two
instances of this structure for TCP and MPTCP. Add a pointer to this structure
in NVMe tcp_ctrl. Then, define a new MPTCP transport ops, which is the same
as the TCP one, only the name is different. When allocating a new tcp_ctrl,
initialize its pointer to a different instance based on the transport name is
"tcp" or "mptcp". Afterwards, we access the instance through the pointer in
tcp_ctrl, use this instance to create the socket and change its behavior.
What do you think of this approach?

## Slide 12
Discussion
mptcpize / mptcpify tools do not work on NVMe TCP
Keep the NVMe code unchanged, can we just use MPTCP tools to convert NVMe TCP to use MPTCP by force? The answer is no.
NVMe MPTCP vs. Block multiqueue
Can NVMe MPTCP work with Block multiqueue? The answer is yes. All queues - both admin queue and I/O queues - are MPTCP connections.
How to select MPTCP?
-> A new transport type?
-> A TCP variant?
A new transport type:
+ straightforward
- Update of the NVMe protocol -> How?
A new TCP 'variant':
+ smaller update of the protocol
-> How: using Transport Specific Address Subtype (TSAS) to represent a new Protocol Type
NVMe MPTCP vs. NVMe multipath
Can NVMe MPTCP work with NVMe multipath? Both names contain 'multipath'. The answer is yes. (I/O policy)
12/15
Notes: Here I have listed several frequently asked questions:
1 Can we, keep the NVMe code unchanged, just use MPTCP tools to convert
NVMe TCP to use MPTCP by force?
The answer is no. Tools like mptcpize and BCC mptcpify allow legacy
(ˈleɡ.ə.si old) TCP programs to use MPTCP without code changes - they
dynamically replace TCP socket creation with MPTCP socket creation at
runtime in the path of the socket syscall. NVMe TCP creates sockets
directly from kernel space and does not invoke socket syscalls, so these
tools have no effect. We do need to change the NVMe code to add MPTCP
support.
2 Can NVMe MPTCP work with NVMe multipath? Both of their names contain
'multipath'.
The answer is yes. They work together at different layers. The selftest
of NVMe MPTCP shows that NVME MPTCP can work with different I/O policies,
that is NVMe multipath. They can work together with no conflict.
3 Can NVMe MPTCP work with Block multiqueue?
The answer is yes too. There is not just one TCP connection between
the target and host - NVMe TCP uses block multiqueue to establish several
TCP connections between them. It includes one admin queue for management
traffic and several I/O queues for data traffic. NVMe MPTCP changes all
these TCP connections to MPTCP connections, both the admin queue and the
I/O queues.
4 How to select MPTCP? A new transport type? or A TCP variant?
The current approach is to define a new transport type for MPTCP.
That is straightforward.
Another option is to declare MPTCP as a TCP 'variant'. For example, in
the TSAS (Transport Specific Address Subtype), just as SECTYPE
represents the versions of TLS (1.2 or 1.3), a new PROTOTYPE can be
added here to represent the protocol is TCP, MPTCP or other future
protocols.

## Slide 13
GitHub:
@geliangtang
Email:
geliang@kernel.org
MPTCP Community:
Website: https://www.mptcp.dev/
Repositories: https://github.com/multipath-tcp/
Mailing List: mptcp@lists.linux.dev
Contact information
13/15
Notes: Here is the contact information for myself and the MPTCP community.
You can find me on GitHub, and you can send me an email.

## Slide 14
References
NVMe over MPTCP
https://lore.kernel.org/all/cover.1775047736.git.tanggeliang@kylinos.cn/
mptcp: implement .read_sock and .splice_read
https://lore.kernel.org/all/20260130-net-next-mptcp-splice-v2-0-31332ba70d7f@kernel.org/
MPTCP KTLS support
https://lore.kernel.org/all/cover.1776469068.git.tanggeliang@kylinos.cn/
libnvme: add mptcp trtype
https://lore.kernel.org/all/99f6e63b5c9677f29a9bc8cdd87b2064b258435f.1764206766.git.tanggeliang@kylinos.cn/
fabrics: add mptcp support
https://github.com/linux-nvme/nvme-cli/commit/f468531d0592ad22b71760d883409363b1f8a9d6
tlshd: add mptcp support
https://github.com/oracle/ktls-utils/commit/8fd3c7071e195206c4119575f40546f7243cc4c1
[LSF/MM/BPF TOPIC] NVMe over MPTCP
https://lore.kernel.org/linux-nvme/a9f115aa5719e1088702a3fdeee766a3166611b1.camel@kernel.org/
14/15
Notes: Here are references. If you want to use this feature,
you can find all the patches here.
The last one is the email thread for this topic.
Feel free to reply with any thoughts, suggestions, or questions.

## Slide 15
Questions
15/15
Notes: If you have any questions, we can address them here.
If I can't answer it immediately, I'll follow up with you by email or some other way.
Thank you very much for your interest in NVMe MPTCP.
I know the process will take a long time, but I'll do my best to push this feature upstream.